## Slide 1
EPIK / UNIK
BASIC Training

## Slide 2
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Teaching Pendant

## Slide 3
Main Screen button
Emergency stop button
Touch screen
Power and Error Indicator
Axis operation
Jog buttons
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Teaching Pendant

## Slide 4
Automatic Operation
Stop
Manual Operation
Step by Step Operation
Robot Use / No Use
(This button controls Interlock signals)
Overall Velocity
Homing (goes to Wait position) (Press & Hold)
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Teaching Pendant

## Slide 5
Status Bar

## Slide 6
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Operation mode
Auto
Program execution state
On operation
Paused
Stopped
Execution mode
Auto
Step
Status bar
Manual
You can modify programs
only in Manual mode.

## Slide 7
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Operation mode
Auto
Manual
Program execution state
On operation
Paused
Stopped
Execution mode
Auto
Step
You can change programs
only in Manual mode.
Current Mold file name
Current sub-program name.
“MASTER” must be loaded.
Status bar

## Slide 8
z
Robot Status
Operation Space / Reference
Referenced
Emergency Stop Button Status
Unreferenced
Robot In Use (No permission given to the machine)
Robot No Use (All permission given to the machine,
also the machine can be run by hand without the robot)
Status bar

## Slide 9
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Robot Status
Operation Space / Reference
Referenced
Emergency Stop Button Status
Unreferenced
In Use (No IMM machine control)
No Use (No robot control)
Status bar

## Slide 10
z
- Administrator (level 16) –allow to access entire systems in controller (PW: pass)
- Service (level 15) – allow to change the settings and edit the basic programs (PW: service)
- Teacher (level 7) – allow to access the basic settings and programs (PW: teacher)
- Operator (level 1) – only allow to control the robot operation in auto or manual (PW: operator)
Accessible areas in controller are differ by user level.
Status bar

## Slide 11
Auto
Manual
or
Robot In Use
(No permits to IMM)
Robot No Use
(No robot contol)
or
Robot Speed

## Slide 12
Main Screen

## Slide 13
z
Main Screen
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Product Tab
Shows production information
By turning on this option, robot will proceed whole dry cycle with a lower speed.
By turning on this option, robot will only run for one cycle then stop.
Open Origin screen for referencing. Detail will be shown later page.
OFF
ON
OFF
ON

## Slide 14
z
Main Screen
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Info Tab
Shows current status of the robot
<Example>
WAIT: IMM
WAIT: Safety Door
WAIT: Rotation Complete

## Slide 15
z
Main Screen
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Report Tab
Shows warning & error message logs

## Slide 16
z
Main Screen
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Main screen setting buttons
Menu: Go to other setting buttons
Mold : Mold file setting screen
Speed: Detail speed setting screen
Timer: Delay time setting screen

## Slide 17
z
Menu - Mold
Load, create, copy, and delete the mold files
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Yellow highlighted mold name = current loaded
*Changes are allowed only in manual operation state.

## Slide 18
z
Menu - Speed
Adjust speed of each steps
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
③
①
④
②

## Slide 19
z
Menu - Timer
Adjust delay times
before a step.
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Adjust times for Method confirming signals
On/Off button
Notes: The robot checks if the vacuum suction cup successfully grabbed the parts.

## Slide 20
z
Menu - Timer
Adjust delay times
before a step.
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Decide whether or not
to use the Vac. confirmation sensors or Gripper sensors.
On/Off button
Notes: The robot checks if the vacuum suction cup successfully grabbed the parts.

## Slide 21
z
Main Screen
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
By pressing MENU button,
other setting buttons show up

## Slide 22
z
Main Screen
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Parameters: Mode setting screen
Pos: Position setting screen
Prog: line-by-line program screen

## Slide 23
Teaching Positions

## Slide 24
z
Menu - Position

## Slide 25
z
Menu - Position
Select the position you want to teach

## Slide 26
z
Menu - Position
1. Move the robot manually.
2. Press

## Slide 27
z
Robot Action
③
①
④
②
  ① Waiting position (=Home position)
  ② Takeout position
  ③ Up position
  ④ Main Release position
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com

## Slide 28
z
Menu - Position
Position of waiting for the mold opening. Robot moves to this position:
1. After referencing.
2. When homing button is pressed & held
Waiting position
(= Home position)

## Slide 29
z
Menu - Position
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Takeout position

## Slide 30
z
Menu - Position
Up position
Up position
Position of moving up after taking out.
Check “Vacuum Confirmation” at this position.

## Slide 31
z
Menu - Position
Main Release position
Release position
Product
Conveyor
Position of releasing the product. (vacuum, chuck, or gripper)
If stacking or palletizing, this position will be the 1st releasing position.

## Slide 32
z
Menu - Position
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
The easiest teaching sequence of Four(4) basic positions
Teach Takeout position first
Teach Up & Waiting position
Teach Main Release position
③
①
④
②

## Slide 33
z
Menu - Position
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
③
①
④
②
  (Use Main Gripper for Sprue picking)
  Separate Sprue runner and part(s)

## Slide 34
z
Menu - Position
Reject position
Position of releasing the rejected product or the initial products.
③
①
④
②
  Reject
(this position can be the same as “Sub-Release Position”

## Slide 35
z
Menu - Position
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Outside Wait position
Waiting on the mold to be opened in the outside of machine area
Normal Wait position

## Slide 36
z
Menu - Position
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Outside Wait position
Position of waiting or the mold to be opened in a section outside the traversing mold
Normal Wait position

## Slide 37
z
Menu - Position
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Outside Wait position
Pre-Waiting Position
③
①
④
②
Outside Wait
|
① Wait
|
② Takeout
|
③ Up
|
④ Release

## Slide 38
z
Menu - Parameter
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
All the actions of the robot are set
in this screen. Changes are allowed only in manual state.
Parameter Setting Screen

## Slide 39
z
Menu - Parameter

## Slide 40
z
Menu - Parameter

## Slide 41
z
Menu - Parameter
Press here

## Slide 42
Select what method to use
<example>
Gripper

## Slide 43
z
Menu - Parameter
If Debug Mode is marked, administrator can view the entire program while robot is running

## Slide 44
Set when to rotate EOAT
TRAVERSE MOVE

## Slide 45
Set when to rotate EOAT
TRAVERSE MOVE

## Slide 46
Set when to rotate EOAT
TRAVERSE MOVE

## Slide 47
z
Menu - Parameter
If Debug Mode is marked, administrator can view the entire program while robot is running

## Slide 48
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
③
①
④
②
  OFF setting:
  Not using sub release position for runner.
  All methods OFF at main release position
Setting runner release timing

## Slide 49
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
③
①
④
②
Traverse OFF Setting
Drop the Runner(s) First
Then the part(s).
Setting runner release timing
TRAVERSE MOVE

## Slide 50
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
③
①
④
②
Traverse Return OFF Setting
Drop the part(s) first
Then, drop the runner(s) while returning to WAIT position.
Setting runner release timing
TRAVERSE RETURN MOVE

## Slide 51
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
③
①
④
②
In Mold Setting
After taking out the part & runner,
Kick back,
then release gripper,
then moves up.
Setting runner release timing

## Slide 52
z
Menu - Parameter
If Debug Mode is marked, administrator can view the entire program while robot is running

## Slide 53
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Controls Ejector Forward Timing
No Use Setting
Machine controls ejector forward timing

## Slide 54
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Controls Ejector Forward Timing
Before Take-Out
The robot arrives at take out position,
Robot sends Ejector Forward Permit signal to the machine.
EJECTOR

## Slide 55
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Controls Ejector Forward Timing
Down
Before kick forward,
Robot sends Ejector Forward Permit signal to the machine.
And then kick forward.
EJECTOR

## Slide 56
z
Menu - Parameter
If Debug Mode is marked, administrator can view the entire program while robot is running

## Slide 57
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Robot waits for
Ejector Retract Complete signal
from the machine
USE Setting
After grabbing the part,
Before kick back,
Robot waits for the signal from the machine.
To prevent the robot moving up and damage while ejector is forward.
EJECTOR

## Slide 58
z
Menu - Program
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Line-by-line programming
For Advanced Level

## Slide 59
z
Menu - Signals
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com

## Slide 60
z
Menu - Signals
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com

## Slide 61
z
Menu - Signals
Interlock tab
From IMM
to Robot
From Robot
to IMM
Giving permission to IMM
If “MOLD CLOSE” is unchecked,
The machine cannot close the mold.
If “MOLD CLOSE DONE” is on,
The robot arm cannot go down to the mold area.
If “SAFETY DOOR” is off,
The robot cannot run with auto.
If “EJECTOR FWD” is unchecked,
The machine cannot pull Ejector out.
This button controls all the permission to machine at once.

## Slide 62
z
Menu - Signals
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
You can manually turn on/off vacuum, chuck, main gripper, and user outputs.
After installing EOAT & vacuum cups,
you can turn on vacuums
and check if air connection is okay or EOAT grabs parts well.
ON
OFF

## Slide 63
Soft Torque

## Slide 64
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Enabling the SoftTorque will make Y axis “Soft” by turning off servo motor.
Robot arm can be pushed back by the ejector easily.
To protect pins and increase durability.
Soft Torque

## Slide 65
z
Menu - Parameter

## Slide 66
z
SoftTorque
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Change Chuck Delay in Timer menu to set the SoftTorque duration
Use
Use

## Slide 67
Under cut

## Slide 69
z
Menu - Parameter
If Debug Mode is marked, administrator can view the entire program while robot is running

## Slide 70
Robot can move up to 9 positions
before kick back and move up

## Slide 72
Referencing

## Slide 73
After Referencing done,
z
Main screen - Origin
*When you try to re-reference the robot, the alarm will go off, and it is normal. In that case, reset alarm and reference again.
When power on, the robot needs “Referencing”
When referencing,
The robot automatically finds each axis value.

## Slide 74
z
Main screen - Origin
Origin screen button
*When you try to re-reference the robot, the alarm will go off, and it is normal. In that case, reset alarm and reference again.

## Slide 75
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Checking Errors and Warnings

## Slide 76
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Warning
Error
Status bar
When you see Warning, it is normal.
When you see Error, the robot stops and triggers buzzer.

## Slide 77
z
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Warning
Error
Status bar

## Slide 78
z
Error
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
Click or button
to see the messages.

## Slide 81
Starting
Automatic Operation

## Slide 82
z
Automatic Operation
<How to start Auto operation>
In order to start Auto,
the robot must to be at home position (wait position)
Press homing button on keypad

## Slide 83
z
Automatic Operation
2. Put the Robot No Use state
Press robot no use button on keypad

## Slide 84
z
Automatic Operation
3. Start Press machine auto / semi-auto

## Slide 85
z
Automatic Operation
4. When Mold is completely closed
& injecting
Press homing button for 1 second

## Slide 86
z
Automatic Operation
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com
5. Press Auto operation button

## Slide 87
Stopping the operation

## Slide 88
z
Stopping
Press button to stop the robot.
Then stop selection window pops up
When is pressed, it is temporary stop and
will be able to resume at the current position by pressing Auto button.
When is pressed, the current cycle will be stopped.
HYROBOTICS CORP
5319 Brown Ave.
St. Louis MO, 63120, USA
http://www.hyrobotics.com

## Slide 89
Quick Reference
For starting up the Robot

## Slide 90
5. Basic Parameter Settings
6. Position Settings
3. Log in
2. Reference
1. Power on the robot
4. Make a New Mold File & Load
Move the robot with jog buttons, and
Quick Reference
- Administrator (level 16) allow to access entire systems in controller
- Service (level 15) allow to change the settings and edit the basic
programs
Teacher (level 7) allow to access the basic settings and programs
Operator (level 1) Only allow to access to operation
If the buttons are grayed out,
press manual operation.
Mold file name must start with a letter, not number.
After new mold file is created, load it.
Check whether the robot is at a safe place before moving on to the step 2.
If it is not at a safe place, then please move to a safe place by using Manual jog button.
- Method: Vacuum & Gripper
- Clamp Side or Nozzle Side Take out?
- EOAT Rotation – when to rotate?
- Ejector Forward Control (If applicable)
- Waiting Position
- Up Position
- Takeout Position
- Main Release Position
If the robot doesn’t move, check if it is referenced & in manual mode.
Press position button
DANGER
Beware of moving objects. Do not enter in the operation range
Press menu button

## Slide 91
8. Check other signals
9. Start Auto Run
7. Check IMM / Interlock Signals
Quick Reference
Press Robot In Use / No Use button, check interlock signals.
Start IMM
with Auto run
Press signal button
Go to Interlock tab
No control on IMM
Robot In Use
Able to control on IMM
Robot No Use
During Injection cycle,
Press Homing button
For 1 second.
Press Auto Run button.
Put “Robot No use” state

## Slide 92
Thank you
Let's move on to hands-on training.